Liber version 2.3.0

# Sanguine Modules Mutants
It is our sincere hope these modules excite you as much as they did us when creating them and fuel all your musical ventures!
In a hurry? If you are looking for the instructions for a specific module, use the handy provided table of contents (it is clickable!). The base modules are presented in alphabetical order, followed by their alternative firmwares, if any are available.
# The Modules
## Aleae – Bernoulli Gates
A two channel randomizer for your voltages. Whenever a trigger is received in one of the two inputs, a virtual coin is tossed, its results affecting the output in different ways.
This handy utility module is great for generative patches or adding movement to your existing one.
This module can be driven at audio levels to create a noise generator.
This module is polyphonic and will produce a different coin toss for every channel present in the input.
We aim for this module to serve your chaotic needs!
Based on Mutable Instruments’ Branches.

### The Controls

Aleae consists of two identical sections at the top and at the bottom, only the top section is pictured here.
#### Knobs and buttons
COIN MODE: this button selects between the two available “coin toss” modes:
  - Direct mode: the LED in the coin mode button is lit green. Whenever a trigger is received, a virtual coin is tossed, if it lands on “heads” OUTPUT A (3) gets a trigger or gate (if LATCH MODE (B) is enabled); if the result is “tails” the trigger or gate goes to OUTPUT B (4).
  - Toggle mode: the LED in the coin mode button is lit red. In this mode the outcome of the coin toss works as follows:
    - “Heads”: continue sending the trigger to the same output it was being sent to after the last toss.
    - “Tails”: the trigger is now sent to the opposite output until a new tails result is obtained.
    When the PROBABILITY KNOB (C) is set to its maximum value a trigger toggles between the two outputs.
1. LATCH MODE: this button toggles LATCH MODE on and off. When LATCH MODE is enabled the button glows orange.
  When this mode is off and a trigger is received, a trigger is, in turn, sent to the output decided by the coin toss depending on the COIN MODE (A) setting.
  When this mode is on, a gate is sent to one of the outputs and remains open (or high) until a trigger is received and a new output is selected, or this mode is disabled.
2. PROBABILITY KNOB: this knob changes the odds to obtain a particular result from the coin toss.
  In Direct mode turning it all the way counter-clockwise makes every trigger go to OUTPUT A (3) (“heads”) and turning it completely clockwise selects OUTPUT B (4) (“tails”) every time.
  In Toggle mode turning it all the way to the left makes every trigger go to OUTPUT A (3) and setting it to its maximum value to the right makes outputs switch on every coin toss.

#### Inputs and outputs
1. Trigger input: a trigger here makes the module throw a virtual coin and send a trigger or gate to one of the outputs depending on the result and your settings.
2. Probability CV input: change the odds of getting “heads” or “tails” along with the PROBABILITY KNOB (C).
3 and 4. Outputs: a 10V trigger or gate, depending on your LATCH MODE (B) settings, will be sent to one of these, according to the rules stated above, whenever a trigger is received in Trigger input (1).
## Apices – Multifunction Gap Filler
A two-channel multi-mode trigger/gate processor and noise maker. This fun module offers a lot of functionality that is made easier with our no holds barred interface. We hope this module can keep your beats kicking!
Based on Mutable Instruments’ Peaks.
This manual covers basic operation; but some modes are better understood by connecting the module to a scope and experimenting with it.

### The Controls

#### Knobs and buttons
MODE: selects one of the ten available modes for both channels or the currently selected channel (EXPERT MODE (B) and (C) dependent).
The selected mode is displayed for each channel using one of the displays to the left of the MODE knob and the LEDs around it.
The modes and their display are as follows (hardware easter-egg modes are marked with ▀ in the display; hardware secret modes are marked with &, and hardware disabled modes enabled in Apices are marked with @)
MODE	Display
Envelope	ENVELOPE
LFO	LFO
Tap LFO	TAP LFO
Drum generator	DRUM GENERAT
Sequencer	SEQUENCER▀
Trigger delay/shaper	TRG. SHAPE▀
Trigger stream randomizer	TRG. RANDOM▀
Digital drum synth	DIGI. DRUMS▀
Number station	NUMBER STAT&
Bouncing ball	BOUNCE BALL@

The different modes and how the knobs affect them are described in the Module modes section.
1. CHANNEL SELECT: selects between channels 1 and 2 when EXPERT MODE (C) is enabled, when it is disabled this button has no function.
  The selected channel is shown using the red LEDs to the left of the mode displays: both LEDs are lit when EXPERT MODE is disabled, and either 1 or 2 blink using different rhythms when EXPERT is enabled to indicate the channel you are currently editing.
  When EXPERT MODE is enabled this button glows either green or yellow depending on the channel selected for edition; the LEDs around SPLIT (G) (see below) change color, following this button, to show the channel the knobs are affecting.
2. EXPERT MODE TOGGLE: enables and disables EXPERT MODE.
  This module is quite versatile: when operating in standard mode (EXPERT MODE disabled) whatever mode you set using the knob is applied to both channels (indicated by both red LEDs next to the mode displays staying steadily lit). EXPERT MODE lets you control each channel independently, selecting modes and parameters separately for each one without affecting the other (check the Context menu section below for a note about the knobs).
  When this mode is enabled the button glows blue and the CHANNEL SELECT button is ready for action, glowing either green or yellow depending on the channel selected for edition.
  This mode offers complete, granular control of every parameter for each channel at the expense of complexity.
D, E, H, I: these red and blue knobs set the parameters for the currently selected mode and are dependent on it. The OLED displays adjacent to each knob display terse descriptions of which parameter a given knob affects and to which channels it applies, according to mode selections.
Examples:
- The module is set to standard mode (see above) twin (see below) LFO mode: the knob labeled “1” affects the Frequency for both channels and its display reads “1&2. Frequency”, while the knob labeled “3” affects the waveform variation for both channels and its display reads “1&2. Wave. Var.”.
- The module is set to standard mode (see above) SPLIT (G) (see below) Drum generation mode: the knob labeled “1” affects the tone for the bass drum in channel 1 and its display reads “1. BD Tone”, while the knob labeled “3” affects the tone for the snare drum in channel 2 and its display reads “2. SD Tone”.
- The module is set to EXPERT MODE (C) (see above); channel 2 is selected, and its mode is Envelope: all knobs affect only this channel and, in this case, the knob labeled “1” affects the envelope’s attack, its display reads “2. Attack”, and the knob labeled “3” affects the envelope’s sustain, it’s display reads “2. Sustain”.
F, J: manual triggers for channel 1 and 2, respectively.
SPLIT MODE: this button switches standard mode (see above) between twin and split modes. When SPLIT MODE is enabled this button glows red. It is disabled in EXPERT MODE (see above).
When the module is set to twin mode (SPLIT MODE red light is off) both red knobs and both blue knobs affect different parameters for both channels of the currently selected mode. The LEDs beside the knobs glow purple to show both channels are combined. In this mode you get more control over every parameter but less granularity between channels.
When the module is set to SPLIT MODE the button glows red, the red knobs affect parameters for channel 1 while the blue knobs affect parameters for channel 2. The LEDs next to the red knobs glow red to indicate those knobs affect channel 1 and the LEDs next to the blue knobs glow blue to convey those knobs affect channel 2. In this mode you get more granularity over channel parameters at the expense of less control over individual parameters. For complete control… use EXPERT MODE!

#### Inputs and outputs
1. Trigger 1 input: receives trigger signals for channel 1.
2. Trigger 2 input: receives trigger signals for channel 2.
3. Channel 1 output: emits channel 1 signals.
4. Channel 2 output: emits channel 2 signals.

### The context menu

Apices offers the standard VCV Rack standard context menu with one addition:
Knob pickup (snap): when using EXPERT mode and switching between the two channels the knobs immediately affect the parameters of the newly selected channel with their current positions. To prevent this and make the knobs affect the parameters of the newly selected channel only after they have been moved to their previous value within that channel enable this menu option (disabled by default).

### Module modes
The OLED screens always display what the knobs affect in your selected configuration.
Whenever a trigger is mentioned below it refers to either a trigger from the jack input or a button press.
Modes are presented as they are displayed on the matrix screen.
#### ENVELOPE
Your classic envelope generator. Triggers start and hold the envelope.
Knobs
	TWIN & EXPERT	SPLIT
Knob 1	Ch. 1 & 2 Attack	Ch. 1 Attack
Knob 2	Ch. 1 & 2 Decay	Ch. 1 Decay
Knob 3	Ch. 1 & 2 Sustain	Ch. 2 Attack
Knob 4	Ch. 1 & 2 Release	Ch. 2 Decay

#### LFO
A low-frequency oscillator for your all modulation needs. Triggers reset the waveform cycle.
Knobs
	TWIN & EXPERT	SPLIT
Knob 1	Ch. 1 & 2 Frequency	Ch. 1 Frequency
Knob 2	Ch. 1 & 2 Waveform, from left to right: / Sine / Linear slope / Square / Steps / Random	Ch. 1 Waveform
Knob 3	Ch. 1 & 2 Waveform variation: / Sine: wavefolder / Slope: Ascending / Triangle / Descending balance / Square: pulse-width / Steps: number of steps / Random: interpolation method	Ch. 2 Frequency
Knob 4	Ch. 1 & 2 Phase on restart	Ch. 2 Waveform

#### TAP LFO
A pair of low-frequency oscillators with tap tempo. Triggers set the period of the LFO oscillations. Apices can learn irregular trigger sequences.
Knobs
	TWIN & EXPERT	SPLIT
Knob 1	Ch. 1 & 2 Amplitude	Ch. 1 Waveform
Knob 2	Ch. 1 & 2 Waveform	Ch. 1 Waveform variation
Knob 3	Ch. 1 & 2 Waveform variation	Ch. 2 Waveform
Knob 4	Ch. 1 & 2 Phase on restart	Ch. 2 Waveform variation

#### DRUM GENERAT
A bass and snare drum generator. Triggers start the drum sounds.
Knobs
	TWIN & EXPERT	SPLIT
Knob 1	Ch. 1 & 2 Base frequency	Ch. 1 Tone
Knob 2	Ch. 1 & 2 Frequency modulation ("Punch" for BD, "Tone" for SD)	Ch. 1 Decay
Knob 3	Ch. 1 & 2 High-frequency content ("Tone" for BD, "Snappiness" for SD)	Ch. 2 Tone
Knob 4	Ch. 1 & 2 Decay	Ch. 2 Snappy

#### SEQUENCER▀
Just what it says on the tin.
In TWIN and EXPERT modes the module is a 4 step mini-sequencer with each knob controlling a step. Channel 1 is clocked by Trigger 1 and reset by Trigger 2; Channel 2 is clocked by Trigger 2.
In SPLIT mode the module is a dual 2 step mini-sequencer. No reset is available and each channel has its own clock controlled by its respective trigger.
Knobs
	TWIN & EXPERT	SPLIT
Knob 1	Ch. 1 & 2 Step 1	Ch. 1 Step 1
Knob 2	Ch. 1 & 2 Step 2	Ch. 1 Step 2
Knob 3	Ch. 1 & 2 Step 3	Ch. 2 Step 1
Knob 4	Ch. 1 & 2 Step 4	Ch. 2 Step 2

#### TRG. SHAPE▀
Trigger delayer / shaper. A trigger starts a trigger/gate sequence as configured by the knobs.
Knobs
	TWIN & EXPERT	SPLIT
Knob 1	Ch. 1 & 2 Pre-delay	Ch. 1 Delay
Knob 2	Ch. 1 & 2 Gate duration	Ch. 1 Number of repeats
Knob 3	Ch. 1 & 2 Delay	Ch. 2 Delay
Knob 4	Ch. 1 & 2 Number of repeats	Ch. 2 Number of repeats

#### TRG. RANDOM▀
Trigger stream randomizer. Delay! Repeat! Burst! Get surprised! A trigger has a chance to start a burst of triggers as configured by the knobs.
Knobs
	TWIN & EXPERT	SPLIT
Knob 1	Ch. 1 & 2 Probability of accepting incoming triggers	Ch. 1 Acceptance/regeneration probability
Knob 2	Ch. 1 & 2 Probability of regenerating triggers after the delay	Ch. 1 Delay
Knob 3	Ch. 1 & 2 Delay time	Ch. 2 Acceptance/regeneration probability
Knob 4	Ch. 1 & 2 Jitter	Ch. 2 Delay

#### DIGI. DRUMS▀
Synthesized FM drums! Synthesized FM drums! Get your FM drums here! A trigger starts the drum sound.
Knobs
	TWIN & EXPERT	SPLIT
Knob 1	Ch. 1 & 2 Frequency	Ch. 1 BD presets morphing
Knob 2	Ch. 1 & 2 FM intensity	Ch. 1 BD presets variations
Knob 3	Ch. 1 & 2 FM and AM envelope decay time[1]	Ch. 2 SD presets morphing
Knob 4	Ch. 1 & 2 Color. / At 12 o'clock, no modification is applied to the oscillator signal. / Turn right to increase the amount of noise (for snares). / Turn left to increase the amount of distortion (for 909 style kicks).	Ch. 2 SD presets variations
[1] The FM envelope has a shorter decay than the AM envelope, but the two values are tied to this parameter.

#### NUMBER STAT&
Number station. A mode reminiscent of one of those mysterious number stations, it simulates a noisy AM receiver.
A trigger in Trigger 1 generates one of several digital tones in Channel 1.
A trigger in Trigger 2 generates a voice that speaks one of several different numbers in Channel 2.
Knobs
	TWIN & EXPERT	SPLIT
Knob 1	Ch. 1 & 2 Frequency	Ch. 1 Frequency
Knob 2	Ch. 1 & 2 Variation probability	Ch. 1 Variation probability
Knob 3	Ch. 1 & 2 Noise	Ch. 2 Frequency
Knob 4	Ch. 1 & 2 Distortion	Ch. 2 Variation probability

#### BOUNCE BALL@
Bouncing ball mode. This envelope generator produces signals not unlike bouncing a ball in a basketball court.
Experiment with the parameters and an oscilloscope to get a feel (and visual representation) of how the different parameters affect the envelope.
A trigger throws the ball.

Knobs
	TWIN & EXPERT	SPLIT
Knob 1	Ch. 1 & 2 Gravity	Ch. 1 Gravity
Knob 2	Ch. 1 & 2 Bounce	Ch. 1 Bounce
Knob 3	Ch. 1 & 2 Amplitude	Ch. 2 Gravity
Knob 4	Ch. 1 & 2 Velocity	Ch. 2 Bounce

#### Parameters
- Gravity: how fast the ball drops to the ground: the further clockwise the knob is, the floatier the ball gets.
- Bounce: how much potential energy the ball keeps when falling to the ground. Setting the knob to high clockwise values can make your ball bounce forever (paired with a high gravity this can also make your ball bounce really high!).
- Amplitude: how much force is applied to the initial ball throw. The further the knob is counterclockwise the lower the ball starts when triggered. A fully counterclockwise knob means the ball doesn’t get off the ground at all.
- Velocity: how much the ball travels forward initially. Lower, counterclockwise values, produce envelopes with an initial sharper peak.
## Mutants Blank – Rack sleekerizer
It’s not Mutable or Audible; but who doesn’t want a lovely goblin sitting on their Rack along with the Mutants logo?
Makes your Rack look sleek.
Mutants don’t control, like Machete don’t text.
Bypassing the module turns its lights off.

## Funes – Macro oscillator
Featuring twenty four synthesis models that range from filtered classic wave shapes to synthetic hi-hats, Funes is a polyphonic macro oscillator that caters to your every musical need.
Funes is based on Mutable Instruments’ well known macro oscillator “Plaits”, with the last released firmware: 1.2.
This manual covers basic operation; but a lot of enjoyment comes from experimentation and discovery. Have fun!

### The Controls

#### Knobs
MODEL: twist it back and forth to select the synthesis model. The available models are separated in three banks of eight.
Each of the LEDs at the top represent one of the models and reflect both the selected model and the bank it’s contained in using one of three colors.
The model banks are separated as follows: pitched (green LEDs), noise/percussive (red LEDs) and new synthesis (orange LEDs). The character display uses an eight letter code to present your selection.
The available synthesis models are:
Model #	Model	Display	LEDs color	Note[2]
1	Classic wave shapes with filter.	FLTRWAVE	Orange	C0
2	Phase distortion and modulation	PHASDIST	Orange	C#0
3	6-operator FM 1	6 OP.FM1	Orange	D0
4	6-operator FM 2	6 OP.FM2	Orange	D#0
5	6-operator FM 3	6 OP.FM3	Orange	E0
6	Wave terrain synthesis	WAVETRRN	Orange	F0
7	String machine emulation	STRGMACH	Orange	F#0
8	Chiptune	CHIPTUNE	Orange	G0
9	Pair of classic waveforms	DUALWAVE	Green	G#0
10	Waveshaping oscillator	WAVESHAP	Green	A0
11	Two operator FM	2 OP.FM	Green	A#0
12	Granular formant oscillator	GRANFORM	Green	B0
13	Harmonic oscillator	HARMONIC	Green	C1
14	Wavetable oscillator	WAVETABL	Green	C#1
15	Chords	CHORDS	Green	D1
16	Vowel and speech synthesis	VOWLSPCH	Green	D#1
17	Granular cloud	GR.CLOUD	Red	E1
18	Filtered noise	FLT.NOIS	Red	F1
19	Particle noise	PRT.NOIS	Red	F#1
20	Inharmonic string modeling	STG.MODL	Red	G1
21	Modal resonator	MODALRES	Red	G#1
22	Analog bass drum	BASSDRUM	Red	A1
23	Analog snare drum	SNARDRUM	Red	A#1
24	Analog hi-hat	HI-HAT	Red	B1
[2] Only available when “C0 model modulation” is checked in the context menu.

Synthesis models can also be selected directly using the context menu (see below).
Depending on the selected model, the module controls change different parameters.
For a more in depth explanation of the specific models and how the controls behave when they are selected, please refer to the Module Modes section.
1. FREQUENCY (coarse): its range can be adjusted using the “Frequency mode” item in the context menu. By default it is eight octaves (C0-C8). It also offers “Octaves” and “LFO” modes.
2. FREQUENCY ROOT: when “Octaves” is selected as the “Frequency mode” this knob controls the root note.
3. HARMONICS: model dependent tone control. In general it controls the frequency spread in the tone.
4. TIMBRE: model dependent tone control. In general it controls the “darkness” of the tone.
5. Attenuverters for the TIMBRE, FM and MORPH CV inputs. When the TRIGGER (3) input is patched and the corresponding CV is left unpatched, the attenuverters adjust the modulation amount from the internal decaying envelope generator. So… be warned, if you disconnect a CV input and the TRIGGER (3) patched, any attenuverter value other than “0” will allow the internal envelope to take over.
6. LOW PASS GATE RESPONSE: controls the response of the internal low pass gate from VCFA (counter clockwise) to VCA (clockwise).
7. LOW PASS GATE DECAY: adjusts the ringing time of the internal low pass gate and the decay time of the internal envelope.
8. MORPH: model dependent tone control. In general it controls lateral timbral variations.

#### Inputs and outputs
MODEL selection CV: this input has two modes of operation that depend on your context menu selection:
  - C0 model modulation (monophonic) unchecked (default): when the input is patched, two or more LEDs (depending on polyphony) light up. The blinking LED indicates the central value (the selected model) while the steady LEDs indicate the currently active one for each polyphonic channel. The input voltage functions as an offset to the currently selected central value: negative voltages decrease it and positive voltages increase it. This behavior is the closest to the original “Plaits” with the addition of polyphony.
  - C0 model modulation (monophonic) checked: when the input is patched, the notes C0 to B1 select the current model. Selection is absolute and not influenced by the manually selected model.
In both modes the display updates, by default, to reflect the currently active model for the first, if polyphonic, or only channel connected to the input. This behavior can be disabled in the context menu (see below).
1. CV Inputs for the TIMBRE, FM and MORPH parameters.
2. TRIGGER: serves four different purposes:
  - Triggers the internal decaying envelope generator.
  - Excites the physical and percussive models.
  - If the LEVEL input (4) is not patched, it strikes the internal low-pass gate.
  - Samples and holds the value of the MODEL CV input (1).
1. LEVEL: opens the internal low pass gate; it also acts as an accent control when triggering physical or percussive models.
2. V/Oct: controls the fundamental frequency of the produced sound, from -3 to +7 octaves relative to the root note set by the FREQUENCY (B) knob.
3. CV Input for the HARMONICS (D) parameter.
4. OUT: main output signal (model dependent).
5. AUX: carries a variant or by-product dependent on the OUT (7) output signal (model dependent).

### The context menu

The Funes context menu offers the standard VCV Rack standard context menu with several additions:
- Low CPU (disable resampling): if your computer is struggling enabling this will save some CPU at the expense of sound quality.
- Frequency mode: sets the mode for the FREQUENCY (B) knob.
- Reset custom data for the current engine: some of the models in the “New synthesis models” bank allow the use of custom data. This menu option clears it and loads the built-in default.
- Load custom data for current engine: loads custom data for one of the following models:
  - 6-operator FM models.
  - Wave terrain synthesis.
  - Wavetable synthesis.
Data must be prepared as a .bin file using the editor available here:
https://github.com/tobiza/Plaits-Editor/tree/8190119e5c0e06b495e46eef62d8ed5ce874b53b
In order to use the editor you need to download the code and run it locally in your web browser (tested with Firefox).
- Pitched models, Noise/percussive models and New synthesis models: the items in the sub-menus directly select specific synthesis models.
- Display follows modulated model: when enabled, the LED display changes to reflect the model currently selected by the voltage present in the MODEL CV input (1). If you want the display to only reflect the model selected using the knob or don’t like the effect, disable this option. Enabled by default.
- C0 model modulation (monophonic): when enabled, the selected model is changed by sending note voltage values to the MODEL CV input. Selection is absolute. This disables the default Plaits-like behavior and is monophonic only. Disabled by default.

### Module Modes
The modes are presented with the name that appears on the display to make finding parameters easier.
#### FLTRWAVE
Classic wave shapes with filter.
Controls
Knobs
HARMONICS	Resonance and filter character: / CCW: gentle 24dB/octave / CW: harsh 12dB/octave
TIMBRE	Filter cutoff
MORPH	Waveform and sub level
Outputs
OUT	LP output
AUX	12dB/octave HP output

#### PHASDIST
Phase distortion and modulation.
Controls
Knobs
HARMONICS	Distortion frequency
TIMBRE	Distortion amount
MORPH	Distortion asymmetry
Outputs
OUT	Synchronized carrier (phase distortion)
AUX	Free running carrier (phase modulation)

#### 6 OP.FM1, 6 OP.FM2, 6 OP.FM3
2 voice, 6 operator fm synthesizer. 3 models with banks of 32 presets each.
Controls
Knobs
HARMONICS	Preset selection
TIMBRE	Modulators level
MORPH	Envelope and modulation stretching / time travel.
Inputs
TRIGGER	The two voices play alternatively when a trigger is received. If TRIGGER is not patched, a single voice plays as a drone and MORPH allows time travel along envelopes and modulations.
LEVEL	Velocity control (loudness or timbre, depending on preset).
Outputs
OUT	Synchronized carrier (phase distortion)
AUX	Free running carrier (phase modulation)

#### WAVETRRN
Wave terrain synthesis. Use 2D maps as sound! Continuous interpolation between eight terrains.
Controls
Knobs
HARMONICS	Terrain
TIMBRE	Path radius
MORPH	Path offset
Outputs
OUT	Direct terrain height (z axis)
AUX	Terrain height as phase distortion (sin(y+z))

#### STRGMACH
String machine emulation with stereo filter and chorus.
Controls
Knobs
HARMONICS	Chord
TIMBRE	Chorus/filter amount
MORPH	Waveform
Outputs
OUT	Voices 1&3 predominantly
AUX	Voices 2&4 predominantly

#### CHIPTUNE
Four variable square voices or arpeggios.
Controls
Knobs
HARMONICS	Chord
TIMBRE	Arpeggio type or chord inversion
TIMBRE attenuverter	Envelope shape
MORPH	PW/Sync
Inputs
TRIGGER	Arpeggiator clock
Outputs
OUT	Square wave voices
AUX	NES triangle voice

#### DUALWAVE
Virtual-analog synthesis of classic waveforms.
Controls
Knobs
HARMONICS	Detuning between the two waves
TIMBRE	Variable square: from narrow pulse (CCW) to full square (12 o’clock) to hardsync formants (CW)[3]
MORPH	Variable saw: from triangle (CCW) to saw (12 o’clock) with an increasingly wide notch (Nodi’s CSAW).[4]
Outputs
OUT	Main signal
AUX	Sum of two hard sync’ed waveforms: shape is controlled by MORPH and detuned by HARMONICS
[3] A narrow pulse results in silence.
[4] A wide notch results in silence.

#### WAVESHAP
An asymmetric triangle processed by a wave shaper and a wave folder.
Controls
Knobs
HARMONICS	Wave shaping waveform
TIMBRE	Wave folder amount
MORPH	Waveform asymmetry
Outputs
OUT	Main signal
AUX	Variant with different wave folder curve

#### 2 OP.FM
Two sine oscillators modulating each other’s phase.
Controls
Knobs
HARMONICS	Frequency ratio
TIMBRE	Modulation index
MORPH	Feedback. Operator 2 modulates its own phase (past 12 o’clock: rough) or operator 1’s phase (before 12 o’clock: chaotic)
Outputs
OUT	Main signal
AUX	Sub-oscillator

#### GRANFORM
A simulation of formants and filtered wave forms through the multiplication, addition and synchronization of sine wave segments.
Controls
Knobs
HARMONICS	Frequency ratio between formants 1 and 2
TIMBRE	Formant frequency
MORPH	Formant width and shape. Controls the shape of the window by which a sum of two synchronized sine oscillators is multiplied.
Outputs
OUT	Main signal
AUX	Simulation of filtered wave forms by windowed sine waves. HARMONICS controls the filter type (peaking, LP, BP, HP).

#### HARMONIC
An additive mixture of harmonically related sines.
Controls
Knobs
HARMONICS	Frequency ratio between formants 1 and 2
TIMBRE	Formant frequency
MORPH	Formant width and shape. Controls the shape of the window by which a sum of two synchronized sine oscillators is multiplied.
Outputs
OUT	Main signal
AUX	Simulation of filtered wave forms by windowed sine waves. HARMONICS controls the filter type (peaking, LP, BP, HP).

#### WAVETABL
Four banks of 8x8 wave forms, accessible by row and column. With or without interpolation.
Controls
Knobs
HARMONICS	Bank selection. The first 4 are interpolated banks (CCW); the next 4 are the same banks, in reverse order, without interpolation (CW). / Bank A: harmonically poor waveforms from additive synthesis (sine harmonics, drawbar organ wave forms) / Bank B: harmonically rich wave forms from formant synthesis or wave shaping / Bank C: wave tables from the Shruti-1 / Ambika, sampled from classic wave table or ROM playback synthesizers. / Bank D: a semi-random permutation of wave forms from the other 3 banks.
TIMBRE	Row index. Waves are sorted by spectral brightness in banks A-C
MORPH	Column index
Outputs
OUT	Main signal
AUX	Low-fi (5 bit) output

#### CHORDS
Four note chords played by virtual analogue oscillators (emulating a stack of harmonically related square or saw tooth wave forms generated by vintage string & organ machines), or wave table oscillators.
Controls
Knobs
HARMONICS	Chord type. / From left to right: / Octave / 5 / sus4 / m / m7 / m9 / m11 / 69 / M9 / M7 / M
TIMBRE	Chord inversions and transpositions
MORPH	Wave form. The first half of the knob goes through a selection of string machine like raw wave forms; the second half scans a small wave table with 16 wave forms.
Outputs
OUT	Main signal
AUX	Root note of the chord

#### VOWLSPCH
A bunch of speech synthesis algorithms.
Controls
Knobs
HARMONICS	Crossfades between formant filtering, SAM and LPC vowels, then goes through several banks of LPC words.
TIMBRE	Species selection, from Daleks to chipmunks. This parameter shifts the formants up or down independently of the pitch, or underclocks/overclocks the emulated LPC chip (compensating to maintain pitch)
MORPH	Phoneme or word segment selection. / When HARMONICS is past 11 o’clock, a list of words can be scanned by turning this knob or sending CV to its input
FM Attenuverter	Word intonation
MORPH Attenuverter	Word speed
INPUTS
TRIGGER	Utter word
Outputs
OUT	Main signal
AUX	Unfiltered vocal chords signal

#### GR.CLOUD
A swarm of 8 enveloped saw tooth waves.
Controls
Knobs
HARMONICS	Pitch randomization
TIMBRE	Grain density
MORPH	Grain duration and overlap. When fully CW, the grains merge into each other resulting in a stack of eight randomly frequency modulated wave forms
Outputs
OUT	Main signal
AUX	Variant with sine wave oscillators

#### FLT.NOIS
Variable clock white noise processed by a resonant filter.
Controls
Knobs
FREQUENCY	Filter cutoff frequency
HARMONICS	Filter response: from LP to BP to HP
TIMBRE	Clock frequency
MORPH	Filter resonance
Inputs
V/OCT	Filter cutoff frequency
Outputs
OUT	Main signal
AUX	Variant with two band-pass filters. Their separation is controlled by the HARMONICS knob.

[•]
[•] From the original Plaits manual, used with permission via the CC-BY-SA 3.0 license governing that document.
#### PRT.NOIS
Dust noise processed by networks of all-pass or band-pass filters.
Controls
Knobs
HARMONICS	Amount of frequency randomization
TIMBRE	Particle density
MORPH	Filter type: / Reverberating all-pass network before 12 o’clock / Increasingly resonant band-pass filters past 12 o’clock
Outputs
OUT	Main signal
AUX	Raw dust noise

#### STG.MODL & MODALRES[‡]
[‡] This mode uses its own decay envelope and filter. The internal LPG is disabled for it. A TRIGGER input triggers the signal; but doesn’t strike the LPG. When the TRIGGER input is patched, the LEVEL input works as an accent control.
A mini Rings[5]; please refer to the Rings manual at https://pichenettes.github.io/mutable-instruments-documentation/modules/rings/manual/ for more information about inharmonic string synthesis and modal resonators.
[5] The processor in the original hardware module is not as powerful as Rings’, so this module is limited to 3 voices of polyphony in inharmonic string modeling mode, and 1 voice of polyphony with 24 partials in modal resonator mode. This module does not let you control the position of the excitation, which is set to 25% of the length of the string/bar/tube.
Controls
Knobs
HARMONICS	Amount of inharmonicity or material selection
TIMBRE	Excitation brightness and dust density
MORPH	Decay time (energy absorption)
Inputs
TRIGGER	Excite the string or resonator. / When this input is patched the string is excited by a short burst of filtered white noise or by a low-pass filtered click. / When this input is not patched the string or resonator is excited by particle noise.
Outputs
OUT	Main signal
AUX	Raw exciter signal

#### BASSDRUM‡
Analog bass drum. Behavioral simulation of the circuits from classic drum machines.
Controls
Knobs
HARMONICS	Attack sharpness and amount of overdrive
TIMBRE	Brightness
MORPH	Decay time
Inputs
TRIGGER	When this input is not patched a continuous tone is produced.
Outputs
OUT	Bridget T-network excited by shaped pulse
AUX	Frequency modulated triangle VCO turned into a sine with a pair of diodes, shaped by dirty VCA.

#### SNARDRUM‡
Analog snare drum. Like a marching band!
Controls
Knobs
HARMONICS	Balance of the harmonic and noisy components
TIMBRE	Balance between the different modes of the drum
MORPH	Decay time
Outputs
OUT	Bridget T-networks, one for each mode of the shell, excited by a nicely shaped pulse, and some band filtered noise
AUX	Frequency modulated pair of sine VCOs, mixed with high pass filtered noise.

#### HI-HAT[‡]
[‡] This mode uses its own decay envelope and filter. The internal LPG is disabled for it. A TRIGGER input triggers the signal; but doesn’t strike the LPG. When the TRIGGER input is patched, the LEVEL input works as an accent control.
Analog hi-hat. Metallic counter-point
Controls
Knobs
HARMONICS	Balance of metallic and filtered noise
TIMBRE	High-pass filter cutoff
MORPH	Decay time
Outputs
OUT	6 square oscillators generating a harsh, metallic tone mixed with clock noise; sent to a high-pass filter and, finally, through a dirty transistor VCA.
AUX	3 pairs of square oscillators ring modulating each other, sent through a clean, linear VCA.

## Nodi – Macro Oscillator X
A deep, powerful digital sound source featuring 47 synthesis models (and a fixed morse code generator). We hope this module can serve as your sonic army knife.
Nodi is based on Mutable Instruments’ “Braids” module. The module includes the sub-oscillator modes from the 1.9 unreleased firmware.
Basic operation is covered in this manual; but playing around and experimenting with the module is sure to be rewarding.

### The Controls
#### Knobs and buttons
1. META: controls the Meta-Modulation option.
  When this option is enabled, the button glows red and voltage applied to the FM CV input (3) selects the currently active synthesis model. The voltage acts as an offset from the model selected by the MODEL (H) knob: negative voltages select lower models and positive voltages select higher models.
  Discontinuities may be heard when switching models.
  The currently selected model always appears in the LED display at the top.
  When this option is disabled, the button is off and the FM CV input (3) does Frequency modulation, as you expect.
  Disabled by default.
2. TIMBRE: controls the main evolution and motion of the timbre.
3. COARSE: controls oscillator tuning in big steps. Its range is affected by the RANGE (U) knob.
4. MORS: enables and disables the Morse code easter egg from the original module.
  When this mode is enabled, the button glows white and excerpt from Pynchon's The Crying of Lot 49 is output as Morse code.
  The excerpt is the following:
  The Scope proved to be a haunt for electronics assembly people from Yoyodyne. The green neon sign outside ingeniously depicted the face of an oscilloscope tube, over which flowed an ever-changing dance of Lissajous figures. Today seemed to be payday, and everyone inside to be drunk already. Glared at all the way, Oedipa and Metzger found a table in back. A wizened bartender wearing shades materialized and Metzger ordered bourbon. Oedipa, checking the bar, grew nervous. There was this je ne sais quoi about the Scope crowd: they all wore glasses and stared at you, silent. Except for a couple-three nearer the door, who were engaged in a nose-picking contest, seeing how far they could flick it across the room. A sudden chorus of whoops and yibbles burst from a kind of juke box at the far end of the room. Everybody quit talking. The bartender tiptoed back, with the drinks. What’s happening? Oedipa whispered. That’s by Stockhausen.
  TIMBRE (B) controls the symbol duration, and COLOR (R) adds some background noise.
  When this mode is disabled the button is off.
  Disabled by default.
5. FINE: controls oscillator tuning in small steps: -1 to +1 semitones.
6. ATK: controls the attack of the internal VCA AD envelope.[†]
  [†] VCA (I) mode must be enabled for the AD envelope to function.
7. TMBR |\: controls the amount of modulation from the internal AD to the TIMBRE (B)†
8. MODEL: Rock the big knob back and forth to select the synthesis model.
  The knob lights up in different colors depending on the selected model.
  The model’s abbreviation is shown in the LED display at the top of the module. The available models are the following:
Model #	Model	Display
1	Quirky sawtooth	CSAW
2	Triangle to saw	/\\-_
3	Sawtooth wave with dephasing	//-_
4	Wavefolded sine/triangle	FOLD
5	Buzz	uuuu
6	Square sub	SUB-
7	Saw sub	SUB/
8	Square sync	SYN-
9	Saw sync	SYN/
10	Triple saw	//x3
11	Triple square	-_x3
12	Triple triangle	/\\x3
13	Triple sine	SIx3
14	Triple ring mod	RING
15	Saw swarm	////
16	Saw comb	//uu
17	Circuit-bent toy	TOY*
18	Low-pass filtered waveform	ZLPF
19	Peak filtered waveform	ZPKF
20	Band-pass filtered waveform	ZBPF
21	High-pass filtered waveform	ZHPF
22	VOSIM formant	VOSM
23	Speech synthesis	VOWL
24	FOF speech synthesis	VFOF
25	12 sine harmonics	HARM
26	2-operator phase-modulation	FM
27	2-operator phase-modulation with feedback	FBFM
28	2-operator phase-modulation with chaotic feedback	WTFM
29	Plucked string	PLUK
30	Bowed string	BOWD
31	Blown reed	BLOW
32	Flute	FLUT
33	Bell	BELL
34	Drum	DRUM
35	Kick drum circuit simulation	KICK
36	Cymbal	CYMB
37	Snare	SNAR
38	Wavetable	WTBL
39	2D wavetable	WMAP
40	1D wavetable	WLIN
41	4-voice paraphonic 1D wavetable	WTx4
42	Filtered noise	NOIS
43	Twin peaks noise	TWNQ
44	Clocked noise	CLKN
45	Granular cloud	CLOU
46	Particle noise	PRTC
47	Digital modulation	QPSK
48	Paques morse code[◊]	49
[◊] This mode is only selectable using the MORS (D) button.

Synthesis models can also be selected directly using the context menu (see below).
Depending on the selected model, the module controls change different parameters.
For a more in depth explanation of the specific models and how the controls behave when they are selected, please refer to the Module Modes section.
1. VCA: enables and disables the internal AD.
  When it is enabled, the button glows green and the AD envelope (controlled by ATK (F) and DCY (M) affects incoming or auto-generated triggers.
  When it is disabled, the button is off and TRIG (5) works as a sync/reset input.
  Disabled by default.
2. MOD: controls the amount and polarity of modulation applied to the TIMBRE (B) parameter, from the TIMBRE CV input jack (1).
3. ROOT: selects the root note the quantizer builds scales upon. For the quantizer to function QNTZ (L) must be set to a value other than “OFF”.
  The default value is “C”.
4. QNTZ: enables quantization for V/OCT jack incoming voltages.
  Voltages can be quantized to semitones or one of several available scales.
  The selected scale flashes briefly in the LED display.
  The available scales are the following:
Scale	Display
Off	OFF
Semitones	SEMI
Ionian	IONI
Dorian	DORI
Phrygian	PHRY
Lydian	LYDI
Mixolydian	MIXO
Aeolian	AEOL
Locrian	LOCR
Blues major	BLU+
Blues minor	BLU-
Pentatonic major	PEN+
Pentatonic minor	PEN-
Folk	FOLK
Japanese	JAPA
Gamelan	GAME
Gypsy	GYPS
Arabian	ARAB
Flamenco	FLAM
Whole tone	WHOL
Pythagorean	PYTH
1_4_Eb	EB/4
1_4_E	E /4
1_4_Ea	EA/4
Bhairav	BHAI
Gunakri	GUNA
Marwa	MARW
Shree	SHRI
Purvi	PURV
Bilawal	BILA
Yaman	YAMA
Kafi	KAFI
Bhimpalasree	BHIM
Darbari	DARB
Rageshree	RAGE
Khamaj	KHAM
Mimal	MIMA
Parameshwari	PARA
Rangeshwari	RANG
Gangeshwari	GANG
Kameshwari	KAME
Pa__Kafi	PAKA
Natbhairav	NATB
M_Kauns	KAUN
Bairagi	BAIR
B_todi	BTOD
Chandradeep	CHAN
Kaushik_todi	KTOD
Jogeshwari	JOGE

The default value is “OFF”.
1. DCY: controls the decay of the internal AD envelope generator.[†]
  [†] VCA (I) mode must be enabled for the AD envelope to function.
2. CLR |\: controls the amount of modulation from the internal AD to the COLOR (R).†
3. DRIFT: when this mode is enabled, the button glows yellow and the oscillators drift, as if they were poorly designed.
  When this mode is disabled the button is off and oscillators play nice.
  Disabled by default.
4. FLAT: when this mode is enabled, the button glows orange and oscillators suffer from lower and higher frequencies detuning, to recreate some of the tuning imperfections of VCOs.
  When this mode is disabled oscillators are like rulers.
  Disabled by default.
5. FM|\: controls the amount of modulation from the internal AD to the FM (V).†
6. COLOR: controls a second dimension of sound. The specifics for this knob vary from model to model, consult each model’s description for more details.
7. OCT: transposes notes by octave (-2 to +2).
  Default value is “0”.
8. SIGN: when this mode is enabled, the button glows purple and grungy glitches and imperfections are applied to the output signal.
  When disabled, the button is off and your signals are clean. This is the default value.
9. RANGE: chooses the range of the COARSE (C) knob.
  The current selected range flashes briefly in the LED display.
  The available ranges are:
  - EXT-: adjusts the range of the COARSE (C) knob +/- 4 octaves around the note received on the V/Oct input. A consequence of this is that when no frequency CV signal is sent to the module (i.e. 0V: a very low note!) The COARSE (C) knob will have a bias towards low frequencies, something not always desirable. This is the default range.
  - FREE: adjusts the range of the COARSE (C) knob to +/- 4 octave centered around C3 (261.5 Hz). This is the recommended setting when the module is used with no external signal on the V/Oct CV input.
  - XTND: (extended) provides a larger frequency range, but disables accurate V/Oct scaling as a side effect.
  - 440: locks the oscillator frequency to 440 Hz precisely.
    Helpful for tuning another VCO.
  - LFO: turns the oscillator into an LFO.
1. FM: When Meta-Modulation is disabled, this knob is a frequency modulation attenuverter that controls the amount and polarity of modulation applied to the frequency from the FM CV input jack (3).
  When Meta-Modulation is enabled, this knob is an attenuverter that controls the amount and polarity of modulation applied to MODEL selection from the FM CV input jack (3).
2. TRIG DLY: applies a delay between the moment when a trigger is received and a note is "struck" on the physical models.
3. AUTO: when this mode is enabled, the button glows green and changes in the V/OCT (4) input larger than a semitone generate a trigger. This allows, for example, to excite the physical models or the internal AD generator by a note sequencer without gate outputs.
  When this mode is disabled, the button is off and changes in the V/OCT (4) input are ignored for triggering purposes. An external trigger source connected to the TRIG input (5) is required to produce sound in some models. This is the default.
4. BITS: selects the bit-depth of the data sent to DAC.
5. selects the refresh rate of the DAC.[6]
  [6] Do note that VCV Rack sampling rate affects this. A handful of complex models are rendered internally at 48kHz (instead of 96kHz); so the difference between 48kHz and 96kHz might be non-existent for them. Some of the simpler models are, conversely, rendered internally at 192kHz or 384kHz to reduce aliasing.

#### Inputs and outputs
1. TIMBRE CV: control voltage input for the TIMBRE (B).
  A value of 0V corresponds to the minimum position of the knob and a value of +5V to its maximum.
  This CV is offset by the knob’s current position.
2. COLOR CV: control voltage input for the COLOR (R).
  A value of 0V corresponds to the minimum position of the knob and a value of +5V to its maximum.
  This CV is offset by the knob’s current position.
3. FM CV: CV input for frequency modulation.
  The scale and polarity of this signal is set by the FM (V) attenuverter.
4. V/OCT: 1V/Oct frequency CV input.
5. TRIG: Trigger input; serves three purposes:
  1. Physical models need to be “excited” by an impulse on this input to produce a sound.
  2. The other models will treat triggers as reset signals, bringing the oscillators’ phase to 0.
  3. This input can also be used to trigger an internal AD envelope applied to the parameters of your choice, to create sound animation and attacks without an external envelope module.
6. Signal output. Loudness of the output varies among the different synthesis models.

### The context menu

1. Model: synthesis models (except for the Morse code “Easter egg” can be selected directly using the context menu instead of turning the knob.
2. Low CPU: if your computer struggles with this module, enabling this option can help (at the expense of sound quality).

### Module modes
The modes are presented as they appear on the display to make finding parameters easier.
#### CSAW
Quirky saw. Inspired by a quirk/defect of the Yamaha CS80 saw tooth wave shape: a fixed-width “notch” after the raising edge.
Controls
Knobs
TIMBRE	Width of the notch
COLOR	Depth and polarity (good for phasing effects)

#### /\\-_
Triangle to saw. Produces the classic waveform trajectory from triangle to saw tooth to square to pulse found in synthesizers such as the RSF Kobol or the Moog Voyager.
Controls
Knobs
TIMBRE	Sweep through the wave forms
COLOR	Morph through several tonal characters by increasingly removing the high-frequencies with a 1-pole filter, and recreating them with a wave shaper.

#### //-_
A blend of a saw tooth wave with dephasing control and a square wave with PWM.
Controls
Knobs
TIMBRE	Amount of dephashing or pulse width
COLOR	Morph the wave from saw tooth to square

#### FOLD
Sine and triangle oscillators sent through a wave folder.
Controls
Knobs
TIMBRE	Wave folder strength
COLOR	Balance between the sine and triangle waves

#### uuuu
A digital synthesis algorithm that generates a smooth sequence of wave forms.
Controls
Knobs
TIMBRE	Transition from sine wave to Dirac comb
COLOR	Detuning amount of the two blended wave shapes

#### SUB-
Square sub-oscillator.
Controls
Knobs
TIMBRE	Pulse width
COLOR	Steppiness

#### SUB/
Saw tooth sub-oscillator
Controls
Knobs
TIMBRE	Morph teeth
COLOR	Oscillator phase

#### SYN-, SYN/
Synthesis of the classic 2-oscillator hard-sync patches, with both oscillators emitting square or saw waves.
Controls
Knobs
TIMBRE	Interval between master and slave
COLOR	Oscillator balance

#### //x3, -_x3, /\x3, SIx3
Three saw tooth (or square, triangle, sine) oscillators that can be individually tuned.
Controls
Knobs
TIMBRE	Frequency of the third oscillator relative to the first. Quantized to musical intervals.
COLOR	Frequency of the second oscillator relative to the first. Quantized to musical intervals.

#### RING
Three sine wave oscillators ring-modulated together and colored by a wave shaper.
Controls
Knobs
TIMBRE	Frequency of the second sine wave relative to the first
COLOR	Frequency of the third sine wave relative to the first

#### ////
A swarm of 7 saw tooth waves.
Controls
Knobs
TIMBRE	Saw tooth detuning
COLOR	High pass filter

#### //uu
Generate a saw tooth wave form and send it to a comb filter (tuned delay line).
Controls
Knobs
TIMBRE	Transposition of the delay line frequency
COLOR	Feedback amount and polarity

#### TOY*
Traverse a space of timbres typical of circuit-bent electronic musical toys.
Controls
Knobs
TIMBRE	Toy’s clock rate
COLOR	Glitches or short-circuits on a converter or memory chip's data lines

#### ZLPF, ZPKF, ZBPF, ZHPF
Synthesize in the time-domain the response of a low-pass, peaking, band-pass or high-pass filter excited by classic analog wave forms. Rather.
This model aims at building the filtered wave shape from scratch.
The technique has been used in the Casio CZ or the Roland D series, but is extended here to cover different filter types and wave shapes.
Controls
Knobs
TIMBRE	Filter’s cutoff frequency
COLOR	Modifiy the wave shape: from saw to square to triangle.

#### VOSM
A combination of 3 oscillators arranged in a ring-modulation/hardsync patch to emulate formant synthesis. A technique named VOSIM and described by Kaegi and Tempelaars.
Controls
Knobs
TIMBRE	Relative frequencies of the 2 formants
COLOR	Relative frequencies of the 2 formants

#### VOWL, VFOF
Vowel sounds synthesizer.
VOWL recreates early computer speech synthesis.
VFOF is a simplified version of Rodet's FOF synthesis technique.
Controls
Knobs
TIMBRE	Vowel morphing between a, e, i, o, u
COLOR	Shifts the formants frequency

#### HARM
Additive synthesis by summing 12 sine harmonics.
Controls
Knobs
TIMBRE	Central frequency
COLOR	Distribution of the amplitudes of each of the harmonics around the central frequency

#### FM, FBFM, WTFM
Three different versions of 2-operator phase-modulation synthesis.
FM is a well-behaved implementation.
FBFM uses feedback from the carrier to itself to produce harsher tones.
WTFM uses two feedback paths, from carrier to modulator and carrier to itself to achieve droning, unstable tones.
Controls
Knobs
TIMBRE	Modulation amount
COLOR	Relative frequency interval between modulator and carrier

#### PLUK[‡]
[‡] This mode needs to be excited by a trigger.
Raw plucked string synthesis.
Controls
Knobs
TIMBRE	Damping
COLOR	Plucking position

#### BOWD‡
Bowed string modeling.
Controls
Knobs
TIMBRE	Friction level
COLOR	Bowing position

#### BLOW, FLUT
Reed or flute instrument model.
Controls
Knobs
TIMBRE	Air pressure
COLOR	Instrument geometry

#### BELL‡
Risset additive synthesis model to recreate the tone of a bell.
Controls
Knobs
TIMBRE	Sound dampening
COLOR	Sound inharmonicity

#### DRUM‡
A variant of the BELL model the uses different parameters (partials frequencies and amplitudes) to generate a sound reminiscent of a metallic drum.
Controls
Knobs
TIMBRE	Dampening
COLOR	Brightness

#### KICK[‡]
[‡] This mode needs to be excited by a trigger.
Simulation of the TR-808 bass drum circuit.
Controls
Knobs
TIMBRE	Decay time
COLOR	Brightness

#### CYMB
Raw material for cymbal sound synthesis.
Controls
Knobs
TIMBRE	Band-pass filter cutoff
COLOR	Balance between droning sum of square waves and noise

#### SNAR‡
A simulation of the TR-808 snare drum circuit.
Controls
Knobs
TIMBRE	Balance between the two resonator modes (“tone”)
COLOR	Amount of noise (“snappy”)

#### WTBL
Classic implementation of wave table synthesis.
Controls
Knobs
TIMBRE	Sweep the wave table
COLOR	Select a wave table (20 available). Wave forms are interpolated when traveling through the same wave table; but not when switching among different ones

#### WMAP
Two dimensional 16x16 wave table with 256 wave forms. Similar sounding waves forms are laid out adjacent to each other. X and Y are smoothly interpolated when scanning.
Controls
Knobs
TIMBRE	Scan the table in the X direction
COLOR	Scan the table in the Y direction

#### WLIN
One dimensional scanning through every Nodi wave table.
Controls
Knobs
TIMBRE	Move through the waves
COLOR	Interpolation method: / 7 o’clock: no interpolation / 10 o’clock: interpolate between samples but not waves / 12 o’clock: always interpolate / Beyond 12 o’clock interpolation is applied between waves; but playback resolution decreases.

#### WTx4
Four voice variant of WLIN.
Controls
Knobs
TIMBRE	Morph through a small selection of 16 waves
COLOR	Select the harmonic structure between the 4 voices, from a predefined set of chords. / At 7 o’clock all voices play the same note with a variable amount of detuning.

#### NOIS
Noise through a state variable filter.
Controls
Knobs
TIMBRE	Filter resonance
COLOR	Cross-fade between the low-pass and high-pass outputs of the filter

#### TWNQ
A "Twin Peaks" model that generates white noise and processes it with two band-pass filters (resonators). Both filters track the main frequency.
Controls
Knobs
TIMBRE	Q factor of the filters
COLOR	Filter spacing

#### CLKN
Generate random samples at a given rate determined by the main pitch control.
Controls
Knobs
TIMBRE	Periodicity of the generator (up to a 2 sample cycle)
COLOR	Quantization level (from 2 to 32 distinct values)

#### CLOU, PRTC
Granular synthesis models that create natural textures by mixing short grains of windowed sine waves (CLOU) or short decaying "pings" (PRTC).
Controls
Knobs
TIMBRE	Density and overlap of the grains
COLOR	Grain frequency randomization

#### QPSK
Generate, in the audio frequency range, the kind of modulated signals used in digital telecommunication systems.
A 16-byte synchronization frame is sent on every trigger or every 256 data bytes.
Controls
Knobs
TIMBRE	Bit-rate
COLOR	Sets an 8-bit value which is modulated into the carrier using QPSK modulation.

#### 49
This “Easter egg” mode is described in depth in the MORS (D) section of the Knobs and buttons chapter.
## Contextus – Resurgent Macro Oscillator X
A remixed digital sound source featuring 57 synthesis models.
Contextus is based on the Renaissance firmware for the Mutable Instruments “Braids” module.
This manual documents the changes Contextus offers when compared to the basic Nodi module; for basic operating instructions and descriptions of the modes already present in the base Nodi module consult its manual elsewhere in this document.
We hope this module grants you some really tasty and fat sounds!
### The changes

- New algorithms have been added:
  - The Commodore 64 “Software Automated Mouth” (SAM) robotic text-to-speech algorithm.
  - Five diatonic chord algorithms.
  - Five “chord stack” algorithms.
- A few things have been removed:
  - The “Easter egg” Morse code is gone, along with the “MORS” button on the face plate.
  - QPSK algorithm.
- An algorithm was replaced:
  - The WTx4 algorithm has been replaced with the WTCH, an algorithm that offers more features.
- Contextus differs from the hardware firmware in the following way:
  - The option to reverse the encoder knob is inaccessible: we wired the encoder properly.
The module controls and menus remain the same, and their letter or number reference has not been changed in the diagram above, if you need a refresher on their basic functions, check the manual for Nodi.
A description of the new synthesis modes and the parameters the knobs alter for them follows.
### New module modes
The modes are presented as they appear on the display to make finding parameters easier.
#### SAM1, SAM2
The classic Commodore 64 robotic voice ready to be used in your rack!
Each SAM model contains 16 different words and is similar to a granular sampler.
A TRIG (5) makes SAM play the selected word starting at the current grain. In this case, the V/OCT (4) controls both the speed and pitch of the output.
The selected word can be scrubbed with the TIMBRE (B) knob. This way an envelope can control the speed without altering the pitch.
SAM1 and SAM2 differ only in their word lists.
Controls
Knobs
TIMBRE	Scrub through the selected word; a fully CCW knob plays the first grain of the word while a fully CW knob plays the last
COLOR	Change the selected word

#### \\CH, -_CH, /\CH, SICH, WTCH
Play diatonic chords using different wave forms (saw, square, triangle, sine and wave table).
When the quantizer (QNTZ (L) is disabled, this mode behaves like the WTx4 mode in the base Nodi module; but when it is enabled in one of the diatonic modes (dorian, eolian, etc.) The chords stay in key and pick the correct major, minor or extension based on the selected scale and root note.
Controls
Knobs
TIMBRE	This parameter controls different aspects depending on the selected waveform: / \\CH: detuning between the 2 saw waves that make up each note / -_CH: pulse width of the square wave. / /\CH, SICH: the amount of wave folding to apply to each oscillator before summing / WTCH: morph between a small set of wave table entries. The wave table is the same as in the original WTx4 mode
COLOR	The function of this knob depends on the state of the quantizer: / Disabled: blend between 16 predefined chords / Enabled: control chord extensions

#### \\x6, -_x6, /\x6, SIx6, WTx6
6 oscillators starting at the V/OCT input (4), spaced evenly across the currently selected quantizer scale.
Controls
Knobs
TIMBRE	This parameter controls different aspects depending on the selected waveform: / \\x6: detuning between the 2 saw waves that make up each note / -_x6: pulse width of the square wave. / /\x6, x6: the amount of wave folding to apply to each oscillator before summing / WTx6: morph between a small set of wave table entries. The wave table is the same as in the original WTx4 mode
COLOR	The function of this knob depends on the state of the quantizer: / Disabled: control the space (in semitones) between the 6 oscillators / Enabled: control the number of scale steps between oscillators

# Acknowledgments & thanks
Mutable Instruments for designing such wonderful modules.
Tobi for the work on getting the 1.2 Plaits firmware in VCV Rack.
Hemmer for the work on getting Peaks working in VCV Rack.
jpnielsen for helping with builds.
gbrandt1 for the work in porting some alternative firmwares and breaking out the controls in some modules.
Burns Audio for the Renaissance firmware.
Mattias Puech for the Clouds Parasite.
VCV Rack, MindMeld, Venom and Sapphire modules and their authors whose sources inspired the solutions for some of the graphical effects present in the Sanguine Modules plugins.
Everyone in the VCV Rack forum who got excited with my first “Funes” release.
Christy Marx for making me laugh, to this day, whenever I look at the Conquests of Camelot manual cover (and, in turn, inspiring the cover for this one).
# Contact
Found a bug? Have a suggestion? A fix?
Please use the issues section at
https://github.com/Bloodbat/SanguineMutants/
# Disclaimer
This software is provided "as is", without warranty of any kind, express or implied, including; but not limited, to the warranties of merchantability, fitness for a particular purpose and noninfringement. In no event shall the authors or copyright holders be liable for any claim, damages or other liability, whether in an action of contract, tort or otherwise, arising from, out of or in connection with the software or the use or other dealings in the software.
Slight discrepancies between the images on the package, this manual and the final plugin are possible and should not affect functionality in any way.
# Licenses & Copyrights
Sanguine Modules; Sanguine Modules Mutants; Sanguine Modules Monsters, and their respective logos, branding and indications are copyright © 2024 Bloodbat / La Serpiente y la Rosa Producciones.
This plugin is free software: you can redistribute it and/or modify it under the terms of the GNU General Public License as published by the Free Software Foundation, either version 3 of the License, or (at your option) any later version.
Mutable Instruments is a registered trademark.
The original Mutable Instruments code license is:
Copyright Emilie Gillet.
Author: Emilie Gillet (emilie.o.gillet@gmail.com)
Permission is hereby granted, free of charge, to any person obtaining a copy of this software and associated documentation files (the "Software"), to deal in the Software without restriction, including without limitation the rights to use, copy, modify, merge, publish, distribute, sublicense, and/or sell copies of the Software, and to permit persons to whom the Software is furnished to do so, subject to the following conditions:
The above copyright notice and this permission notice shall be included in all copies or substantial portions of the Software.
THE SOFTWARE IS PROVIDED "AS IS", WITHOUT WARRANTY OF ANY KIND, EXPRESS OR IMPLIED, INCLUDING BUT NOT LIMITED TO THE WARRANTIES OF MERCHANTABILITY, FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT. IN NO EVENT SHALL THE AUTHORS OR COPYRIGHT HOLDERS BE LIABLE FOR ANY CLAIM, DAMAGES OR OTHER LIABILITY, WHETHER IN AN ACTION OF CONTRACT, TORT OR OTHERWISE, ARISING FROM, OUT OF OR IN CONNECTION WITH THE SOFTWARE OR THE USE OR OTHER DEALINGS IN THE SOFTWARE.
This manual is © Bloodbat and licensed under CC BY-NC 4.0. Non-commercial use is allowed with appropriate credit and indication of the original license.
The original Mutable Instruments manuals are licensed as CC-BY-SA-3.0 by Émilie Gillet. The modifications in this document are made by Bloodbat. Non-commercial use is allowed with appropriate credit and indication of the original license.
The panel graphics and logos in the res/ folder are copyright © Bloodbat and licensed under CC BY-NC 4.0. Non-commercial use is allowed with appropriate credit and indication of the original license.
The component graphics in the res/components/ directory are copyright © VCV, modified by Bloodbat and licensed under CC-BY-NC 4.0. Non-commercial use is allowed with appropriate credit and indication of the original license.
Dependencies included in the binary distribution may have other licenses. See LICENSE-dist.txt for a full list.

Copyright © 2024 Bloodbat / La Serpiente y la Rosa Producciones.